## Slide 1: Multiplier menia
Team #1
Abdelaziz Salah Mohammed Kotb
Mohammed kamal Mohammed abdulhady

## Slide 2: ABOUT US
We have implemented 6 types of multipliers which are
Verilog (‘*’) version of multiplier
Multiplier Tree (combinational)
Sequential Multiplier using shift & accumulate
Booth Algorithm (Original algorithm as seen in right figure)
Radix-4 Booth Algorithm.
Floating point

## Slide 3: PROBLEM
Sequential Multiplier using shift & accumulate
Mohammed Kamal
Multiplier Tree
Mohammed Kotb
Radix 4 Booth
Abdelaziz Salah
Floating point
Mohammed Abdulhady
Booth
Abdelaziz Salah

## Slide 4
The (*) multiplier
It has nothing to be done, it is already implemented via model sim itself with the most optimized way.

## Slide 5
Booth multiplier
It is implemented according to the same algorithm which was provided in the flow chart, its idea depends on initializing an accumulator register (A) in the beginning of the process after that it add another bit called (q0) concatenating it with the multiplicand, and always check on the last bit of the multiplicand and q0, so we have 3 cases:
(q1q0 == 00 || q1q0 == 11)
  In this case we just apply a shift arithmetic right to this concatenation (AQq0)
(q1q0 == 01)
  In this case we add the value of the multiplicand to the value in the accumulator
  After that we apply a shift arithmetic right to this concatenation (AQq0)
(q1q0 == 10)
  In this case we subtract the value of the multiplicand to the value in the accumulator
  After that we apply a shift arithmetic right to this concatenation (AQq0)
At the end we just get the result from the value stored in
(AQ).

## Slide 6
Radix 4 Booth multiplier
It is an enhanced way to apply the booth algorithm,
It depends on the idea that we have to divide the multiplication process on steps by decoding the operations first after that we apply simple operations according to the values we have fetched.
We follow this algorithm:
Since we have 32 bits multiplier so we will need a 16 bits register to store the operations.
We start from bit number 0 and build a mask from 3 bits and check on the left bit and right bit, and depending on their values we take an operation from the operations table which is shown on the left.
After that we apply these operations on the multiplier value and for each operation we shift left by 2
After that we just add all the results together to be able to get the final answer.
The code | The operation
000 | Multiply by 0
111 | Multiply by 0
001 | Multiply by 1
010 | Multiply by 1
011 | Multiply by 2
100 | Multiply by -2
101 | Multiply by -1
110 | Multiply by -1

## Slide 7
Sequential Multiplier
Sequential Multiplier is an old method to multiply two binary numbers. But it is also relevant in many architecture and it is the base of many newly developed multiplication techniques. The multiplication between a and b is shown below.

## Slide 8
Booth multiplier
It is implemented according to the same algorithm which was provided in the flow chart, its idea depends on initializing an accumulator register (A) in the beginning of the process after that it add another bit called (q0) concatenating it with the multiplicand, and always check on the last bit of the multiplicand and q0, so we have 3 cases:
(q1q0 == 00 || q1q0 == 11)
  In this case we just apply a shift arithmetic right to this concatenation (AQq0)
(q1q0 == 01)
  In this case we add the value of the multiplicand to the value in the accumulator
  After that we apply a shift arithmetic right to this concatenation (AQq0)
(q1q0 == 10)
  In this case we subtract the value of the multiplicand to the value in the accumulator
  After that we apply a shift arithmetic right to this concatenation (AQq0)
At the end we just get the result from the value stored in
(AQ).

## Slide 9
Floating Point Multiplier
In order to handle special cases (i.e: multiplication by NaN, inf, etc), the n_case block will check for special and inputs and overwrite the output to the proper output.If inputs are the not special, the output will be selected from the main floating multiplication unit.Preprocessing: - If one input is subnormal it will be normalized this is handled by a shifter an zero counter.- Each mantissa will have its implicit bit added.Multiplication stage:- each mantissa including implicit bit is multiplied together (using booth)Output stage:- calculate resulting mantissa- calculate resulting exponent (addition of both exponents without their offset)- output flags (overflow, underflow)- select between regular and special case outputs

## Slide 10
Wallace tree multiplier
Is a hardware implementation of a binary multiplier, a digital circuit that multiplies two integers, it uses a selection of full and half adders to sum partial products in stages until two numbers are left.
Wallace multipliers reduce as much as possible on each layer.
The Wallace tree has three steps:
Multiply each bit of one of the arguments, by each bit of the other.
Reduce the number of partial products to two by layers of full and half adders
Group the wires in two numbers, and add them with a conventional adder
Compared to naively adding partial products with regular adders, the benefit of the Wallace tree is its faster speed. It has O ( log ⁡ n ) reduction layers, but each layer has only O(1) propagation delay. A naive addition of partial products would require O(lg^2 (n)) time.
These computations only consider gate delays and don't deal with wire delays, which can also be very substantial.

## Slide 11: Star multiplier
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 12: Booth multiplier
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 13: Radix 4 booth
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 14: Sequential
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 15: Tree multiplier
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 16: Floating point
Simple and quick to build
Creates spaces for community interactions
Reduces carbon footprint

## Slide 17: THANK YOU
Team #1
Faculty of Engineering
Cmp2024
Delivered to TA Dina Tantawy and TA Amr Ahmed.